## Slide 1: Virtual Private Networks

## Slide 2: Part 1: “Practical” VPNs

## Slide 3: Open issues
Collision domains are unsecure
Employees often need to remote access to corporate network resources
  The Internet traffic is much more vulnerable to eavesdropping than the one that runs in an internal company network (think at a hotel wifi).
More remote offices may need to have access to the same resources
General privacy needs with respect to ISPs, Governments…

## Slide 4: Solution
Idea: simulating a collision domain using an artificial underlying physical network (Internet) as the transmission media and, by means of a tunneling protocol, encapsulating the data to be transmitted (and possibly encrypting it)
Goal: get a transparent and secure subnet at low cost
a secure tunnel is created from the point of origin to the arrival
data can be transmitted both encrypted and signed

## Slide 5: VPN for Roadwarriors

## Slide 6: VPN LAN-2-LAN

## Slide 7: Many-to-many Secured VLAN

## Slide 8: Other goals
Anonimity
Geographic proxying

## Slide 9: Alternatives
Layer 7 Proxying
  Semi-transparent
  (SOCKS5: applications must support it)
  Nontransparent
  (HTTP-based, with redirection)

## Slide 10: VPN Ingredients
A VPN Server
A Tunneling protocol
Confidential
With integrity checks
A user authentication machinery
Must handle individual accounts
Virtual Network cards

## Slide 11: Virtual NICs

## Slide 12: VPN Layer processing

## Slide 13: VPN Processing server side

## Slide 14: Tunnels: client to server VPN traffic

## Slide 15: Tunnels: server to client VPN traffic

## Slide 16: Full Tunnel vs Split Tunnel
Full Tunnel
  the VPN server becomes the default gateway
Split Tunnel
  Only some routes forward to the VPN server

## Slide 17: Advantages of VPN
Cost reduction (for the use of the Internet)
  Connecting remote locations without the costs of a dedicated line
Scalability
  Add a potentially unlimited number of new sections or roadwarriors
Security and protection of data transmitted over the network
Possibility to access the corporate network users outside the company
Protocol independent, no need to support SSL at layer 4-7

## Slide 18: Disadvantages
Overhead and loss of bandwidth
Configuration far from automatic
Vulnerabilities exist, VPNs are not the universal solution
  «Tanto c’ho la VPN», «Tanto c’ho la mascherina»
ONLY the virtual link between client and VPN server is under protection

## Slide 19: Secure VPN
Authentication mechanisms for the endpoints of the tunnel (during the setup of the tunnel)
Transit traffic encryption
The traffic is encrypted and this creates a "Tunnel" between two networks / hosts
The "Secure VPN" have one or more tunnels and each tunnel has two endpoints

## Slide 20: Secure VPNs
To be called Secure, a VPN must provide:
  an authentication system
  the data must be transmitted under encryption and with signatures
  Cryptography must be strong and can be rekeyed over time

## Slide 21: Secure VPNs
Are used:
  to protect the traffic when the Internet is the network of support or if the level of security offered by the underlying network differs from that required by domestic traffic to the VPN
  In a remote access scenario, where a VPN client (end user) connects securely to a remote office network
    For example, utilities offer remote access to employees of an organization

## Slide 22: Secure VPNs
Technologies and protocols used (some non-standard IETF)
  SSH Tunneling
  SSL/TLS VPN (with SSL/TLS)
    OpenVPN
  PPTP/SSTP (with MPPE).
  IPsec ‘pure’
  Ipsec+L2TP+IKEv2

## Slide 23: Obstacles to VPN deployment
TCP Tunnels : Head of the line blocking
  Sequence numbers are a trouble
GRE and IPSec are not NAT friendly
IPSec over UDP is OK, but with smaller MTU

## Slide 24: Security Protocols (Secure VPN)
Ipsec (Internet Protocol Security)
  Developed for IPv6, but also used for IPv4
  Introduction of security
    Traffic encryption: traffic read only by target
    Integrity
    Authentication of peers

## Slide 25: Security Protocols (Secure VPN)
IPsec (Internet Protocol Security)
  Standard
    Encapsulating Security Payload (ESP): provides authentication, confidentiality and integrity check of the message;
    Authentication Header (AH): ensures authentication and integrity of the messagebut does not offer the confidentiality;
    Internet key exchange (IKE): implements "exchange keys" to realize the encrypted stream;
    AH authenticates the complete package, instead ESP authenticates data only.

## Slide 26: VPN with SSH Tunnel
iptables –A FORWARD –i eth1 –d ssh.server –p tcp –dport 22 –j ACCEPT
iptables –A FORWARD –i eth0 –p tcp –sport 22 \
–m state –state ESTABLISHED, RELATED–j ACCEPT

## Slide 27: VPN PPTP+GRE
iptables –A FORWARD –p 47 –d vpn.server –j ACCEPT
iptables –A FORWARD –i eth1 –d vpn.server–p tcp –-dport 1723 –m state –state ESTABLISHED, RELATED–j ACCEPT
iptables –FORWARD –eth0 –p tcp –-sport 1723 \ –m state –state ESTABLISHED, RELATED–j ACCEPT

## Slide 28: Tunneling with IPsec
iptables –A FORWARD –p esp –j ACCEPT
iptables –A FORWARD –i eth1 –p udp –-dport 500 \
–m state –state ESTABLISHED, RELATED–j ACCEPT
iptables –A FORWARD –i eth0 –p udp –-sport 500 \
–m state –state ESTABLISHED, RELATED–j ACCEPT

## Slide 29: Virtual links: other technologies
Protocols used for the Tunneling:
  L2TP (Layer 2 Tunneling Protocol)
  MPLS (Multi-Protocol Label Switching)
  GRE (Generic Routing Encapsulation)
  PPTP(Point-to-Point Tunneling Protocol)
  Ipsec
  IEEE 802.1Q (Ethernet VLANs)

## Slide 30: Tunneling: other technologies
Point to Point Tunneling Protocol (PPTP) | Developed by Microsoft, is a Point to Point Protocol (PPP) extension that encapsulates IP, IPX, NetBEUI into IP packets
Layer 2 Forwarding (L2F) | Developed by Cisco, used for the “tunneling” of link protocols
Layer 2 Forwarding Protocol (L2TP) | Created with an agreement to Microsoft and Cisco, allows the “tunneling” of PPP traffic on several networks. Gives a multi-protocol dial-up service for ISP and POP provider. As L2F, L2TP does not provide encryption.
Socksv5 | L2TP alternative developed by Nec

## Slide 31: Security Protocols (Secure VPN)
Transport Layer Security (SSL/TLS)
  Can be used for tunneling the entire network traffic (SSL/TLS VPN) or to make it secure a individual connection
  SSL (essential for providing remote access to VPN services)
    Advantage of SSL VPN is that it can also be accessed from locations that restrict access to SSL-based Web sites without the support of IPsec.
    SSL-based VPNs may be vulnerable to denial-of-service targeted to TCP connections, being unauthenticated
  Ensures confidentiality and reliability of communications over a public network
  Protects from intrusion, alteration or falsification

## Slide 32: Security Protocols (Secure VPN)
Datagram Transport Layer Security (DTLS)
  Cisco AnyConnect VPN.
  DTLS resolve the HOL problem on TCP
Microsoft Point-to-Point Encryption (MPPE)
  Used with PPTP
  PPTP (point-to-point tunneling protocol):
    Data encryption
    Developed by Microsoft, ensures authentication, encryption and compression of data
  Generic Routing Encapsulation (GRE): GRE creates a virtual link point-to-point and this is done in a way that none of the two ends have to worry about the infrastructure on which the communication passes

## Slide 33: Security Protocols (Secure VPN)
Secure Socket Tunneling Protocol (SSTP) (Microsoft)
  Windows Server 2008, Windows Vista Service Pack 1.
  SSTP tunnels PPP o L2TP traffic via a SSL 3.0 channel
MPVPN (Multi Path Virtual Private Network)
  Developed by Ragula Systems Development Company
SSH VPN -- OpenSSH
  Provides VPN tunneling to ensure secure remote connections to a network

## Slide 34: Security Protocols (Secure VPN)
L2TP (Layer 2 Tunnelling Protocol)
  Secure/Trusted VPN
  Standard IETF
  Is a layer 5 protocol (session) that works as a layer 2 protocol (data link) using UDP packets to encapsulate L2TP packets and to maintain a Point-to-Point connection.
  Has to be combined with another protocol to implement authentication, confidentiality and integrity of data (usually IPSec).
L2TPv3 (Layer 2 Tunnelling Protocol version 3)
  Secure/Trusted VPN
  Evoluzione di L2TP creato come alternativa a MPLS

## Slide 35: IPSec based VPN
Data confidentiality: Encrypts packets before transmission (ESP)
Data integrity: Authenticates packets to help ensure that the data has not been altered during transmission
Data origin authentication: Authenticates the source of received packets, in conjunction with data integrity service (Internet Key Exchange protocol)
Antireplay: Detects aged or duplicate packets, rejecting them

## Slide 36: SSL-based VPN
Alternative to IPSec for remote-access VPNs
SSL provides access special client software
Secure connectivity by authenticating the communicating parties and encrypting the traffic
SSL operates at the session layer and doesn’t not support applications not coded for SSL
SP can provide granular access control, limiting individual users' access to resources
Include application proxies (SSL must be aware of each individual connection )
SSL is computing-intensive (encryption processes )

## Slide 37: Authentication
The tunnel endpoints have to authenticate before establish a secure VPN circuit
  Tunnel End user-created can use passwords, biometrics, two-factor authentication, other encryption methods
  Network-to-network tunnels using passwords or digital certificates, since it must be stored permanently and does not require manual intervention for the activation of the tunnel.

## Slide 38: Part 2: “General” VPNs

## Slide 39: What is a Virtual Private Network in the broad sense
The term is generic, it can describe different configurations of networks and protocols ...
Virtual: it is an artificial network that relies on an underlying physical network
Private: data is transmitted encapsulated and ensuring some form of confidentiality
It works as a “pipe within a pipe” where the outside is formed by the connection of the underlying network
  Internet can be used as a communication platform
  Establishes the logical channels that are totally logic and safe between sections

## Slide 40: Classification (based on ...)
Type of Tunneling protocol
Localization of the "tunnel termination“
  user side (LAN) or network provider
Access type
  site-to-site, remote access connectivity
Guaranteed security level
OSI layer that is exposed to the network connection
  Layer 2 circuits, Layer 3 network connectivity

## Slide 41: Classification

## Slide 42: GARR network

## Slide 44: Traditional classification
Intranet VPN: connecting remote offices or locations of a company
Remote access VPN: connect head office of a company with remote or mobile users
Extranet VPN: connect the central office with partners, customers, suppliers
  Intranet VPN: information security, performance of responses, scalability
  Remote VPN access: strong authentication, efficient system of centralized account management
  Extranet VPN: use of standard and open platforms