## Slide 1: Sistemi Operativi e Reti
Il livello fisico (PHY)

## Slide 2: Il livello fisico
Aspetti importanti:
  Modalità di trasmissione fisica dell’informazione
  Materiali usati
  Standardizzazione di apparati, cavi e connettori

## Slide 3: Il Mezzo trasmissivo
Latenza
Banda
Rapporto segnale/rumore
Spazio e Tempo
Teorema del campionamento
Tasso di trasmissione max (Teorema di Nyquist): C = 2B log2 H
Teorema di Shannon-Hartley: C = B log2(1 + S/N)
Tecniche di trasmissione: binaria, fsk, qam
Suddivisione multicanale

## Slide 4: Manchester encoding
Used in 10BaseT
Each bit has a transition
Allows clocks in sending and receiving nodes to synchronize to each other
  no need for a centralized, global clock among nodes!
Hey, this is physical-layer stuff!

## Slide 5: The Local Loop: Modems, ADSL, and Wireless
The use of both analog and digital transmissions for a computer to computer call. Conversion is done by the modems and codecs.

## Slide 6: Modems
(a) A binary signal
(b) Amplitude modulation
(c) Frequency modulation
(d) Phase modulation

## Slide 7: Modems (2)
(a) QPSK.
(b) QAM-16.
(c) QAM-64.

## Slide 8: Modems (3)
(a) V.32 for 9600 bps.
(b) V32 bis for 14,400 bps.
(a)
(b)

## Slide 9: Mezzi trasmissivi
Hanno anche essi uno spettro, detto spettro di attenuazione
Più lungo è la distanza percorsa dal segnale più è attenuato il segnale
Ma sono possibili anche distorsioni

## Slide 10: Mezzi trasmissivi a guida
Doppino intrecciato
Cavo Coassiale
Fibra Ottica

## Slide 11: Doppino Intrecciato
(a) Category 3 UTP.
(b) Category 5 UTP.

## Slide 12: Cavo Coassiale

## Slide 13: Fibra Ottica
La luce è intrappolata nella fibra

## Slide 14: Trasmissione della luce
Attenuazione della fibra
Lunghezza d’onda = frequenza * velocità del segnale (300’000km/sec)
dB = 20 log10 A

## Slide 15: Fiber Cables
(a) Vista di una fibra singola
(b) Una guaina con tre fibre

## Slide 16: Tecnologie fibra ottica
Full duplex (802.3 esteso su fibra full duplex)
GPON

## Slide 17: Le basi
Analisi di Fourier
Segnali a banda limitata
Massima velocità di un canale

## Slide 18: Ogni segnale ha un suo ‘spettro’
Dipende dalle frequenze in gioco nel segnale
Es. Le voci acute hanno uno spettro spostato sulle frequenze alte, le voci basse hanno uno spettro spostato sulle voci basse
Questo vale anche per i segnali digitali
Maggiore è la banda in bit/sec, più ampio è lo spettro
Limite teorico dato dal teorema di Nyquist
DataRate = 2 S log2 H
Ma più è alto H, più il rapporto segnale rumore è problematico!
Notes: Qui fare disegni alla lavagna

## Slide 19: Segnali a banda (spettro) limitata

## Slide 20: Frequency Division Multiplexing
(a) The original bandwidths.
(b) The bandwidths raised in frequency.
(b) The multiplexed channel.
- Segnali di spettro non sovrapposto possono coesistere!

## Slide 21: Digital Subscriber Lines (3)
A typical ADSL equipment configuration.

## Slide 22: Digital Subscriber Lines (2)
Operation of ADSL/VDSL using discrete multitone modulation.
Usato per realizzazioni Fiber-to-the-street (FTTS/FTTC)

## Slide 23: Attenuazione

## Slide 24: Wifi Standards
https://en.wikipedia.org/wiki/IEEE_802.11ac-2013
https://en.wikipedia.org/wiki/IEEE_802.11ax-2021

## Slide 25: Trasmissione non guidata
The Electromagnetic Spectrum
Radio Transmission
Microwave Transmission
Infrared and Millimeter Waves
Lightwave Transmission

## Slide 26: 802.11: Channels, association
802.11b: 2.4GHz-2.485GHz spectrum divided into 11 channels at different frequencies
  AP admin chooses frequency for AP
  interference possible: channel can be same as that chosen by neighboring AP!
host: must associate with an AP
  scans channels, listening for beacon frames containing AP’s name (SSID) and MAC address
  selects AP to associate with
  may perform authentication [Chapter 8]
  will typically run DHCP to get IP address in AP’s subnet

## Slide 27: IEEE 802.11: multiple access
avoid collisions: 2+ nodes transmitting at same time
802.11: CSMA - sense before transmitting
  don’t collide with ongoing transmission by other node
802.11: no collision detection!
  difficult to receive (sense collisions) when transmitting due to weak received signals (fading)
  can’t sense all collisions in any case: hidden terminal, fading
  goal: avoid collisions: CSMA/C(ollision)A(voidance)
A
B
C
A
B
C
A’s signal
strength
space
C’s signal
strength

## Slide 28: IEEE 802.11 MAC Protocol: CSMA/CA
802.11 sender
1 if sense channel idle for DIFS then
  transmit entire frame (no CD)
2 if sense channel busy then
  start random backoff time
  timer counts down while channel idle
  transmit when timer expires
  if no ACK, increase random backoff interval, repeat 2
802.11 receiver
- if frame received OK
return ACK after SIFS (ACK needed due to hidden terminal problem)
sender
receiver
DIFS
data
SIFS
ACK

## Slide 29: Avoiding collisions (more)
idea: allow sender to “reserve” channel rather than random access of data frames: avoid collisions of long data frames
sender first transmits small request-to-send (RTS) packets to BS using CSMA
  RTSs may still collide with each other (but they’re short)
BS broadcasts clear-to-send CTS in response to RTS
RTS heard by all nodes
  sender transmits data frame
  other stations defer transmissions
Avoid data frame collisions completely
using small reservation packets!

## Slide 30: Collision Avoidance: RTS-CTS exchange
AP
A
B
time
RTS(A)
RTS(B)
RTS(A)
CTS(A)
CTS(A)
DATA (A)
ACK(A)
ACK(A)
reservation collision
defer

## Slide 31: 802.11 frame: addressing
frame
control
duration
address
1
address
2
address
4
address
3
payload
CRC
2
2
6
6
6
2
6
0 - 2312
4
seq
control
Address 2: MAC address
of wireless host or AP
transmitting this frame
Address 1: MAC address
of wireless host or AP
to receive this frame
Address 3: MAC address
of router interface to which AP is attached
Address 3: used only in ad hoc mode

## Slide 32
Internet
router
AP
H1
R1
AP MAC addr H1 MAC addr R1 MAC addr
address 1
address 2
address 3
802.11 frame
R1 MAC addr AP MAC addr
dest. address
source address
802.3 frame
802.11 frame: addressing

## Slide 33
frame
control
duration
address
1
address
2
address
4
address
3
payload
CRC
2
2
6
6
6
2
6
0 - 2312
4
seq
control
Type
From
AP
Subtype
To
AP
More
frag
WEP
More
data
Power
mgt
Retry
Rsvd
Protocol
version
2
2
4
1
1
1
1
1
1
1
1
802.11 frame: more
duration of reserved
transmission time (RTS/CTS)
frame seq #
(for reliable ARQ)
frame type
(RTS, CTS, ACK, data)

## Slide 34: Radio Transmission
(a) In the VLF, LF, and MF bands, radio waves follow the curvature of the earth.
(b) In the HF band, they bounce off the ionosphere.

## Slide 35: Politics of the Electromagnetic Spectrum
The ISM bands in the United States.
http://www.eccsrl.it/html/campi.html
http://www.med.ira.inaf.it/Interferenze_page.htm

## Slide 36: Lightwave Transmission

## Slide 37: Communication Satellites (3)
VSATs using a hub.

## Slide 38: Wireless Local Loops
Architecture of an LMDS system.

## Slide 39: Time Division Multiplexing
The T1 carrier (1.544 Mbps).

## Slide 40: Code Division Multiple Access (CDMA)
unique “code” assigned to each user; i.e., code set partitioning
  all users share same frequency, but each user has own “chipping” sequence (i.e., code) to encode data
  allows multiple users to “coexist” and transmit simultaneously with minimal interference (if codes are “orthogonal”)
encoding: inner product: (original data) X (chipping sequence)
decoding: summed inner-product: (encoded data) X (chipping sequence)

## Slide 41: Advanced Mobile Phone System
(a) Frequencies are not reused in adjacent cells.
(b) To add more users, smaller cells can be used.