## Slide 1: Layer 2 Security
Reti e Sicurezza Informatica - 2011

## Slide 2: 802.11 frame: indirizzamento
frame
control
duration
address
1
address
2
address
4
address
3
payload
CRC
2
2
6
6
6
2
6
0 - 2312
4
seq
control
Address 2: MAC address
mittente
Address 1: MAC address
destinazione
Address 3: MAC address
BSSID
Address 3: usato solo in modalità speciali (WDS)

## Slide 3
Internet
router
AP
H1
R1
AP MAC addr H1 MAC addr R1 MAC addr
address 1
address 2
address 3
802.11 frame
R1 MAC addr H1 MAC addr
dest. address
source address
802.3 frame
802.11 frame: indirizzamento

## Slide 4
frame
control
duration
address
1
address
2
address
4
address
3
payload
CRC
2
2
6
6
6
2
6
0 - 2312
4
seq
control
Type
From
DS
Subtype
To
DS
More
frag
WEP
More
data
Power
mgt
Retry
Rsvd
Protocol
version
2
2
4
1
1
1
1
1
1
1
1
802.11 frame: more
duration of reserved
transmission time (RTS/CTS)
frame seq #
(for reliable ARQ)
frame type
(RTS, CTS, ACK, data)

## Slide 5: 802.11: BSS e ESS
ESSID = stringa che denota un gruppo di AP
BSSID = mac address di un singolo AP
Associazione
  Beacon frames
  Probe frames
  Association requests
  Association responses
  Auth requests
  Auth responses

## Slide 6: Allocazione dei canali

## Slide 7: WLAN open
Equivalente a una rete wired con hub
Possibile sniffing, ESSID e BSSID spoofing
De-authentication attack

## Slide 8: Wep Frame Format

## Slide 9: WLAN WEP
Modalità molto semplice di crittografia a chiave pre-condivisa
Ogni pacchetto viene crittografato in base a
  RC4( Chiave || IV )
IV viene trasmetto in chiaro, per ogni frame
La conoscenza della chiave consente Hub equivalent sniffing
Senza conoscere la chiave è possibile comunque la contraffazione dei frame (manipolando ICV)
ICV = CRC-32

## Slide 10: WEP Authentication (open)

## Slide 11: WEP Shared key authentication

## Slide 12: WEP weaknesses
IV space is 24 bit = 16M
Any IV can be reused at any time
  Allows replay attacks
Can decode RC4 sequence without knowledge of the key
Can find packets with same ICV

## Slide 13: WPA: TKIP encryption scheme

## Slide 14: WPA Personal
A chiave condivisa
  TKIP: sempre RC4 ma IV più lunghi, progressivi e non riusabili. Inoltre è stato aggiunto il MIC (Message integrity check)
WPA2 -> AES e Cipher suite
  Fase di autenticazione in cui vengono scambiate PTK e GTK
La conoscenza della master key non implica la possibilità di osservare il traffico altrui
Possibilità di Re-keying periodico

## Slide 15: Key hierarchy

## Slide 16: WPA Enterprise
Autenticazione via server

## Slide 17: 802.1x Authentication steps

## Slide 18: Step 1: pre-auth

## Slide 19: Step 2: Authentication

## Slide 20: WPA-Personal
Step 2 is not present in WPA1/2-Personal
MK is obtained directly from PMK
PMK (256 bit) is obtained from passphrases:
  PBKDF2 (P, S, c, dkLen) = PMK (see RfC 2898)
Options:
  HMAC-SHA1 «repeated» c times over P and S
  P = passphrase, S = SSID, c = 4096 (!)
  Output: PMK, (dkLen =256 bit long)
Possibility of rainbow table attack
  Rainbow tables: http://www.renderlab.net/projects/WPA-tables/
  Most common SSIDs: http://www.wigle.net/gps/gps//Stat

## Slide 21: Step 3: WPA Authorization process
PTK
PRF-X: RfC 4346

## Slide 22: Other Things to know
De-Authentication  DoS
Rogue APs
  Localization?
WPA2-Enterprise can sometimes be worse than WPA2-Personal
Why ARP Spoofing is still possible?

## Slide 23: Wired & Wireless
MITM attacks
  MAC Spoofing, port stealing (Wired, and Wireless open+wep)
  ARP  IP Spoofing (All)
  DHCP Spoofing (All)
  Broadcast attacks (All)
Wireless
  Open WLANs, WEP WLANs : virtually an Ethernet domain with an hub
  WPA & WPA2 WLANs: private unicast, possibility of user isolation

## Slide 24: Port Stealing: Esempio
C manda un frame a R
Un qualsiasi frame originato da G con MAC di R forza un aggiornamento nella switch table
G cattura i pacchetti destinati a R, li esamina, li filtra, forza R a riaggiornare la switch table e ritrasmette i frame catturati
hub
hub
hub
switch
A
B
C
R
G
H
I
address
interface
A
B
R
G
1
1
2
3
1
2
3
Notes: animazione.

## Slide 25: MAC Spoofing / Flooding
Flooding: inondare lo switch di MAC casuali, fino a saturazione della sua switch table.
Contromisure: port locking.
Domande. Cosa succede in una rete con hub? E in una rete WLAN open? WEP? WPA?

## Slide 26: IP Spoofing in LAN

## Slide 27: IP Spoofing in LAN

## Slide 28: Half mitm

## Slide 29: Contromisure
ARP Watching
Tabelle ARP statiche
ARP Jamming
IP Sec, Tunnels, VPN, SSH

## Slide 30: DHCP Spoofing
Consente Half - MITM
Bisogna essere presenti all’accensione e cercare di assegnare un indirizzo IP predeterminato, un gateway e un DNS
Contromisure:
  Rilevamento di DHCP reply multiple

## Slide 31: Attacchi broadcast
Attacchi broadcast:
  Fingere di avere l’IP della vittima (IP spoof)
  Mandare dei ping broadcast a suo nome
  Le risposte raggiungono la vittima e non l’aggressore
  Necessità delle condizioni adatte (di solito l’aggressore sta fisicamente nella stessa sottorete della vittima)
Aggressore
IP falso: 192.168.0.1
Rete
Vittima
IP: 192.168.0.1
Ignari host della
sottorete

## Slide 32: Contromisure
Limitazione ICMP e altri protocolli broadcast su router e host
Configurazione opportuna firewall
Limiti dell’IP spoofing fuori LAN